## Slide 1: Sportsman Mechanical CDR
12/6

## Slide 2: Agenda
What Is Our Robot?
Chassis
Powertrain
Weapon
Concerns
Next Steps
Q&A

## Slide 3: Lance

## Slide 4: What Is Our Robot?
Lance is a two motor, 4 wheel drive flipper
Features:
  HDPE chassis with foam ablatives
  Long, aluminum flipper
  4 wheel indirect drive
Optimized for Firmware Accessibility and autonomous capabilities
Sportsman Mechanical CDR

## Slide 5: Chassis
Subsystems
Materials
  HDPE internal structure = less dense than metal and good impact toughness
  Foam Bumpers = ablative armor to protect against high-kinetic energy instantaneous attacks
Manufacturability
  HDPE structure=mill
  Foam=scissors, glue
Connections
  Puzzle fits for strength without using screws
    (high stress concentration)
  Foam glued to chassis wall

## Slide 6: Chassis
Subsystems
Design
  Thick HDPE walls (high impact toughness) with puzzle fits to avoid fracturing
  Foam chamfered inwards to save weight and to reduce effectiveness of flippers
  Shape - wider than it is deep to fit internal components, manufacturability
  Open top wheels - no plate on top to save weight, predict little to no impact in area
  Bumpers on three sides to protect non-weapon sides
Weight: 5-5.5 lbs
Price: ~$100

## Slide 7: Powertrain
Subsystems
Final design:
  4 wheels with indirect drive
  2:1 pulley ratio to fit weapon between belts
From calculations:
  angular velocity of wheels required → 752 rpm
  torque needed → .51 Nm
  with 2:1 pulley ratio, this means motor must have at least 1500 rpm and .25 Nm of torque
total weight → 4.5-5 lbs
Price: $350
Notes: brun

## Slide 8: Powertrain
Subsystems
Fingertech 22 and 42T pulleys
  2:1 ratio
  < the 3” diameter of wheels
  many options for belt sizes
5203 Series Yellow Jacket Planetary Gear Motor
  fits specs → 1600 rpm, 12V
  stall torque .53 Nm → 2x the necessary torque of .26 Nm
motor and pulley axle connected by machined threading axle
ball bearings in walls holding wheel axles
Notes: micheele

## Slide 9: Powertrain
BaneBots 2 ⅞ ” wheels
  fit our calculations for a ~ 3” wheel
  have used BaneBots wheels in the past
3000 mAh Lipo Battery
  calculations say we need 9000 mAh at stall torque, very hard to find a battery with this that is light enough
  3000 mAh is fine for what we need, won’t always be running at stall torque
We will only be manufacturing the axles and motor axle
Firmware will be controlling drive motors with an ESC thru Arduino bluetooth module
Subsystems
Notes: molyl

## Slide 10: Weapon
Subsystems
Materials
  Flipper=Aluminum 6061 (stock) Strong, light, and slightly flexible
  Rod=High-strength steel - Heavy but very strong
Manufacturability
  Flipper = Mill + Band saw (water jet if too hard to manufacture)
  Shaft = Bandsaw
  Hub = Mill
  Spacer, Motor, Bearings, Screws = purchased
Connections
  Flipper to shaft = Hub
  Rod to motor = replacing original shaft
    No need for flexible torque coupling plus no products that meet our specifications (must go through powertrain pulleys)

## Slide 11: Weapon
Subsystems
Motor Calculations
  To flip ourselves over - Graph of torque required throughout process (to 90 deg) - max 16Nm
  To lift other robots - max 18Nm
  Motor torque (as listed) = 67Nm
Design Decisions
  No flexible shaft coupling - replaced with steel rod
  ½” wide flipper-stability, allows for thinner flipper end
  No aluminum support for flipper (flipper now aluminum)
  Weight = ~2lb
Price: $226.81

## Slide 12: Concerns
Foam
  may get torn up quickly, especially with saws
  may not do much for impact, not hard enough
Weight
  only about .5 lb wiggle room
3mm axles on drive motors and wheels
  thin diameter, may break
Sportsman Mechanical CDR

## Slide 13: Next Steps
Part Drawings
Meeting with Kinetic to go over all decisions and parts
Adding Final Screws in CAD
Manufacturing Plan
Meetings over winter break
Jan Fab
Sportsman Mechanical CDR

## Slide 14: Thank you! Questions?